## Slide 1: Topic for the class: Instruction Codes Unit 2:Basic Computer Organization and Design Date & Time :19.02.2021 02:00 – 02:50
Y. Madhu Babu
Assistant Professor
Department of EECE
GITAM Institute of Technology (GIT)
Visakhapatnam – 530045
Email: myalaka@gitam.edu

## Slide 2: Contents
1.Instruction Codes
2. Computer Registers
3. Computer Instructions
4. Timing and Control
5. Instruction Cycle
6. Memory Reference Instructions
7. Input-Output and Interrupt
8. Complete Computer Description

## Slide 3: Instruction Codes
The Internal organization of a digital system is defined by the sequence of microoperations it performs on data stored in its registers
The user of a computer can control the process by means of a program
A program is a set of instructions that specify the operations, operands, and the processing sequence
Video Box Position

## Slide 4: Instruction Codes cont.
A computer instruction is a binary code that specifies a sequence of micro-operations for the computer. Each computer has its unique instruction set
Instruction codes and data are stored in memory
The computer reads each instruction from memory and places it in a control register
The control unit interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations
Video Box Position

## Slide 5: Instruction Codes cont.
An Instruction code is a group of bits that instructs the computer to perform a specific operation (sequence of microoperations). It is divided into parts (basic part is the operation part)
The operation code of an instruction is a group of bits that defines certain operations such as add, subtract, shift, and complement
Video Box Position

## Slide 6: Instruction Codes cont.
The number of bits required for the operation code depends on the total number of operations available in the computer
2n (or little less) distinct operations  n bit operation code
Video Box Position

## Slide 7: Instruction Codes cont.
Video Box Position
110010??????????
Op code
Control Unit
Read instruction from memory
It’s an ADD operation
Memory

## Slide 8: Instruction Codes cont.
An operation must be performed on some data stored in processor registers or in memory
An instruction code must therefore specify not only the operation, but also the location of the operands (in registers or in the memory), and where the result will be stored (registers/memory)
Video Box Position

## Slide 9: Instruction Codes cont.
Memory words can be specified in instruction codes by their address
Processor registers can be specified by assigning to the instruction another binary code of k bits that specifies one of 2k registers
Each computer has its own particular instruction code format
Instruction code formats are conceived by computer designers who specify the architecture of the computer
Video Box Position

## Slide 10: Instruction Codes cont. Stored Program Organization
An instruction code is usually divided into operation code, operand address, addressing mode, etc.
The simplest way to organize a computer is to have one processor register (accumulator AC) and an instruction code format with two parts (op code, address)
Video Box Position

## Slide 11: Instruction Codes cont. Stored Program Organization
Video Box Position
Processor register (Accumulator AC)
Opcode
Address
Instruction Format
Binary Operand
Operands (data)
Memory 4096x16
15
12
11
0
15
0
Instructions (program)
15
0
0
15

## Slide 12: Instruction Codes Indirect Address
There are three Addressing Modes used for address portion of the instruction code:
  Immediate: the operand is given in the address portion (constant)
  Direct: the address points to the operand stored in the memory
  Indirect: the address points to the pointer (another address) stored in the memory that references the operand in memory
One bit of the instruction code can be used to distinguish between direct & indirect addresses
Video Box Position

## Slide 13: Instruction Codes Indirect Address
Video Box Position
Opcode
Address
Instruction Format
15
14
12
0
11
0
ADD
457
22
Operand
457
1
ADD
300
35
1350
300
Operand
1350
+
AC
+
AC
Direct Address
Indirect address
Effective address

## Slide 14: Instruction Codes Indirect Address
Effective address: the address of the operand in a computation-type instruction or the target address in a branch-type instruction
The pointer can be placed in a processor register instead of memory as done in commercial computers
Video Box Position

## Slide 15: Computer Registers
Computer instructions are normally stored in consecutive memory locations and executed sequentially one at a time
The control reads an instruction from a specific address in memory and executes it, and so on
This type of sequencing needs a counter to calculate the address of the next instruction after execution of the current instruction is completed
Video Box Position

## Slide 16: Computer Registers cont.
It is also necessary to provide a register in the control unit for storing the instruction code after it is read from memory
The computer needs processor registers for manipulating data and a register for holding a memory address
Video Box Position

## Slide 17: Registers in the Basic Computer
Video Box Position
List of BC Registers
PC
15
0
IR
15
0
TR
7
0
OUTR
15
0
DR
15
0
AC
11
0
AR
INPR
0
7
Memory
4096 x 16
  DR 16 Data Register Holds memory operand
  AR 12 Address Register Holds address for memory
  AC 16 Accumulator Processor register
  IR 16 Instruction Register Holds instruction code
  PC 12 Program Counter Holds address of instruction
  TR 16 Temporary Register Holds temporary data
  INPR 8 Input Register Holds input character
  OUTR 8 Output Register Holds output character
11
0

## Slide 18: Computer Registers Common Bus System
Video Box Position
S2
S1
S0
Bus
Memory unit
4096 x 16
LD INR CLR
Address
Read
Write
AR
LD INR CLR
PC
LD INR CLR
DR
LD INR CLR
AC
Adder
and
logic
E
INPR
IR
LD
LD INR CLR
TR
OUTR
LD
Clock
16-bit common bus
7
1
2
3
4
5
6

## Slide 19: Computer Registers Common Bus System cont.
S2S1S0: Selects the register/memory that would use the bus
LD (load): When enabled, the particular register receives the data from the bus during the next clock pulse transition
E (extended AC bit): flip-flop holds the carry
DR, AC, IR, and TR: have 16 bits each
AR and PC: have 12 bits each since they hold a memory address
Video Box Position

## Slide 20: Computer Registers Common Bus System cont.
When the contents of AR or PC are applied to the 16-bit common bus, the four most significant bits are set to zeros
When AR or PC receives information from the bus, only the 12 least significant bits are transferred into the register
INPR and OUTR: communicate with the eight least significant bits in the bus
Video Box Position

## Slide 21: Computer Registers Common Bus System cont.
INPR: Receives a character from the input device (keyboard,…etc) which is then transferred to AC
OUTR: Receives a character from AC and delivers it to an output
(say a Monitor)
Five registers have three control inputs: LD (load), INR (increment), and CLR (clear)
Register  binary counter with parallel load and synchronous clear
Video Box Position

## Slide 22: Computer Registers Memory Address
The input data and output data of the memory are connected to the common bus
But the memory address is connected to AR
Therefore, AR must always be used to specify a memory address
By using a single register for the address, we eliminate the need for an address bus that would have been needed otherwise
Video Box Position

## Slide 23: Computer Registers Memory Address
Register  Memory: Write operation
Memory  Register: Read operation (note that AC cannot directly read from memory!!)
Note that the content of any register can be applied onto the bus and an operation can be performed in the adder and logic circuit during the same clock cycle
Video Box Position

## Slide 24: Computer Registers Memory Address
The transition at the end of the cycle transfers the content of the bus into the destination register, and the output of the adder and logic circuit into the AC
For example, the two microoperations
DR←AC and AC←DR (Exchange)
can be executed at the same time
This is done by:
Video Box Position

## Slide 25: Computer Registers Memory Address
1- place the contents of AC on the bus (S2S1S0=100)
2- enabling the LD (load) input of DR
3- Transferring the contents of the DR through the adder and logic circuit into AC
4- enabling the LD (load) input of AC
All during the same clock cycle
The two transfers occur upon the arrival of the clock pulse transition at the end of the clock cycle
Video Box Position

## Slide 26: Computer Instructions
Video Box Position
Memory-Reference Instructions (OP-code = 000 ~ 110)
Basic Computer Instruction code format
15 14
12 11
0
I
Opcode
Address
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 27: Computer Instructions
Video Box Position
Memory-Reference Instructions (OP-code = 000 ~ 110)
Basic Computer Instruction code format
15 14
12 11
0
I
Opcode
Address
Register-Reference Instructions (OP-code = 111, I = 0)
Input-Output Instructions (OP-code =111, I = 1)
15
12 11
0
Register operation
0 1 1 1
15
12 11
0
I/O operation
1 1 1 1

## Slide 28
Video Box Position
Hex Code
Symbol I = 0 I = 1 Description
  AND 0xxx 8xxx AND memory word to AC
  ADD 1xxx 9xxx Add memory word to AC
  LDA 2xxx Axxx Load AC from memory
  STA 3xxx Bxxx Store content of AC into memory
  BUN 4xxx Cxxx Branch unconditionally
  BSA 5xxx Dxxx Branch and save return address
  ISZ 6xxx Exxx Increment and skip if zero
  CLA 7800 Clear AC
  CLE 7400 Clear E
  CMA 7200 Complement AC
  CME 7100 Complement E
  CIR 7080 Circulate right AC and E
  CIL 7040 Circulate left AC and E
  INC 7020 Increment AC
  SPA 7010 Skip next instr. if AC is positive
  SNA 7008 Skip next instr. if AC is negative
  SZA 7004 Skip next instr. if AC is zero
  SZE 7002 Skip next instr. if E is zero
  HLT 7001 Halt computer
  INP F800 Input character to AC
  OUT F400 Output character from AC
  SKI F200 Skip on input flag
  SKO F100 Skip on output flag
  ION F080 Interrupt on
  IOF F040 Interrupt off
BASIC COMPUTER INSTRUCTIONS

## Slide 29: Computer Instructions Instruction Set Completeness
The set of instructions are said to be complete if the computer includes a sufficient number of instructions in each of the following categories:
  Arithmetic, logical, and shift instructions
  Instructions for moving information to and from memory and processor registers
  Program control instructions together with instructions that check status conditions
  Input & output instructions
Video Box Position

## Slide 30: Timing & Control
The timing for all registers in the basic computer is controlled by a master clock generator
The clock pulses are applied to all flip-flops and registers in the system, including the flip-flops and registers in the control unit
The clock pulses do not change the state of a register unless the register is enabled by a control signal (i.e., Load)
Video Box Position

## Slide 31: Timing & Control cont.
The control signals are generated in the control unit and provide control inputs for the multiplexers in the common bus, control inputs in processor registers, and microoperations for the accumulator
There are two major types of control organization:
  Hardwired control
  Microprogrammed control
Video Box Position

## Slide 32: Timing & Control cont.
In the hardwired organization, the control logic is implemented with gates, flip-flops, decoders, and other digital circuits.
In the microprogrammed organization, the control information is stored in a control memory (if the design is modified, the microprogram in control memory has to be updated)
D3T4: SC←0
Video Box Position

## Slide 33: The Control Unit for the basic computer
Video Box Position
I
Hardwired Control Organization
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
Control
logic
gates
D
0
15 14 . . . . 2 1 0
4 x 16
Sequence decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
outputs
D
T
T
7
15
0

## Slide 34
Video Box Position
- Generated by 4-bit sequence counter and 4x16 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.

## Slide 35: Timing & Control cont.
A memory read or write cycle will be initiated with the rising edge of a timing signal
Assume: memory cycle time < clock cycle time!
So, a memory read or write cycle initiated by a timing signal will be completed by the time the next clock goes through its positive edge
The clock transition will then be used to load the memory word into a register
The memory cycle time is usually longer than the processor clock cycle  wait cycles
Video Box Position

## Slide 36: Timing & Control cont.
T0: AR←PC
  Transfers the content of PC into AR if timing signal T0 is active
  T0 is active during an entire clock cycle interval
  During this time, the content of PC is placed onto the bus (with S2S1S0=010) and the LD (load) input of AR is enabled
  The actual transfer does not occur until the end of the clock cycle when the clock goes through a positive transition
  This same positive clock transition increments the sequence counter SC from 0000 to 0001
  The next clock cycle has T1 active and T0 inactive
Video Box Position

## Slide 37: Instruction Cycle
A program is a sequence of instructions stored in memory
The program is executed in the computer by going through a cycle for each instruction (in most cases)
Each instruction in turn is subdivided into a sequence of sub-cycles or phases
Video Box Position

## Slide 38: Instruction Cycle cont.
Instruction Cycle Phases:
  1- Fetch an instruction from memory
  2- Decode the instruction
  3- Read the effective address from memory if the instruction has an indirect address
  4- Execute the instruction
This cycle repeats indefinitely unless a HALT instruction is encountered
Video Box Position

## Slide 39: Instruction Cycle Fetch and Decode
Initially, the Program Counter (PC) is loaded with the address of the first instruction in the program
The sequence counter SC is cleared to 0, providing a decoded timing signal T0
After each clock pulse, SC is incremented by one, so that the timing signals go through a sequence T0, T1, T2, and so on
Video Box Position

## Slide 40: Instruction Cycle Fetch and Decode cont.
  T0: AR←PC (this is essential!!)
  The address of the instruction is moved to AR.
  T1: IR←M[AR], PC←PC+1
  The instruction is fetched from the memory to IR ,
  and the PC is incremented.
  T2: D0,…, D7←Decode IR(12-14), AR←IR(0-11), I←IR(15)
Video Box Position

## Slide 41
Video Box Position
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
T1
T0
Common bus
BC Instruction cycle: [Fetch Decode [Indirect] Execute]*
• Fetch and Decode

## Slide 42
Video Box Position
= 0 (direct)
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4
Start
SC  0
DETERMINE THE TYPE OF INSTRUCTION
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.

## Slide 43
Video Box Position
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)
r = D7 I’ T3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11, the ith bit of IR.
- D7 = 1, I = 0
- Register Ref. Instr. is specified in B0 ~ B11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
REGISTER REFERENCE INSTRUCTIONS

## Slide 44
Video Box Position
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to be completed in a CPU cycle
- The execution of MR Instruction starts with T4
MEMORY REFERENCE INSTRUCTIONS

## Slide 45: MEMORY REFERENCE INSTRUCTIONS
Video Box Position
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to be completed in a CPU cycle
- The execution of MR Instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 46: MEMORY REFERENCE INSTRUCTIONScont.
Video Box Position
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
Return address: PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1

## Slide 47: MEMORY REFERENCE INSTRUCTIONScont.
Video Box Position
BSA: executed in a sequence of two micro-operations:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T6: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 48
Video Box Position
Memory-reference instruction
DR M[AR]
DR M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC <- 0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 49: Input-Output and Interrupt
Instructions and data stored in memory must come from some input device
Computational results must be transmitted to the user through some output device
For the system to communicate with an input device, serial information is shifted into the input register INPR
To output information, it is stored in the output register OUTR
Video Box Position

## Slide 50: Input-Output and Interruptcont.
Video Box Position
Input-output
terminal
Serial
communication
interface
Computer
registers and
flip-flops
Printer
Keyboard
Receiver
interface
Transmitter
interface
FGO
OUTR
AC
INPR
FGI
Serial Communications Path
Parallel Communications Path

## Slide 51: Input-Output and Interruptcont.
INPR and OUTR communicate with a communication interface serially and with the AC in parallel. They hold an 8-bit alphanumeric information
I/O devices are slower than a computer system  we need to synchronize the timing rate difference between the input/output device and the computer.
FGI: 1-bit input flag (Flip-Flop) aimed to control the input operation
Video Box Position

## Slide 52: Input-Output and Interruptcont.
FGI is set to 1 when a new information is available in the input device and is cleared to 0 when the information is accepted by the computer
FGO: 1-bit output flag used as a control flip-flop to control the output operation
If FGO is set to 1, then this means that the computer can send out the information from AC. If it is 0, then the output device is busy and the computer has to wait!
Video Box Position

## Slide 53: Input-Output and Interruptcont.
The process of input information transfer:
  Initially, FGI is cleared to 0
  An 8-bit alphanumeric code is shifted into INPR (Keyboard key strike) and the input flag FGI is set to 1
  As long as the flag is set, the information in INPR cannot be changed by another data entry
  The computer checks the flag bit; if it is 1, the information from INPR is transferred in parallel into AC and FGI is cleared to 0
Video Box Position

## Slide 54: Input-Output and Interruptcont.
  Once the flag is cleared, new information can be shifted into INPR by the input device (striking another key)
The process of outputting information:
  Initially, the output flag FGO is set to 1
  The computer checks the flag bit; if it is 1, the information from AC is transferred in parallel to OUTR and FGO is cleared to 0
  The output accepts the coded information (prints the corresponding character)
Video Box Position

## Slide 55: Input-Output and Interruptcont.
  When the operation is completed, the output device sets FGO back to 1
  The computer does not load a new data information into OUTR when FGO is 0 because this condition indicates that the output device is busy to receive another information at the moment!!
Video Box Position

## Slide 56: Input-Output Instructions
Needed for:
  Transferring information to and from AC register
  Checking the flag bits
  Controlling the interrupt facility
The control unit recognize it when D7=1 and I = 1
The remaining bits of the instruction specify the particular operation
Executed with the clock transition associated with timing signal T3
Input-Output instructions are summarized next
Video Box Position

## Slide 57: Input-Output Instructions
Video Box Position
D7IT3 = p
IR(i) = Bi, i = 6, …, 11
INP pB11: AC(0-7)  INPR, FGI  0 Input char. to AC
OUT pB10: OUTR  AC(0-7), FGO  0 Output char. from AC
SKI pB9: if(FGI = 1) then (PC  PC + 1) Skip on input flag
SKO pB8: if(FGO = 1) then (PC  PC + 1) Skip on output flag
ION pB7: IEN  1 Interrupt enable on
IOF pB6: IEN  0 Interrupt enable off

## Slide 58: Program Interrupt
The process of communication just described is referred to as Programmed Control Transfer
The computer keeps checking the flag bit, and when it finds it set, it initiates an information transform (this is sometimes called Polling)
This type of transfer is in-efficient due to the difference of information flow rate between the computer and the I/O device
Video Box Position

## Slide 59: Program Interruptcont.
The computer is wasting time while checking the flag instead of doing some other useful processing task
An alternative to the programmed controlled procedure is to let the external device inform the computer when it is ready for the transfer
This type of transfer uses the interrupt facility
Video Box Position

## Slide 60: Program Interruptcont.
While the computer is running a program, it does not check the flags
Instead:
  When a flag is set, the computer is immediately interrupted from proceeding with the current program
Video Box Position

## Slide 61: Program Interruptcont.
  The computer stops what it is doing to take care of the input or output transfer
  Then, it returns to the current program to continue what it was doing before the interrupt
The interrupt facility can be enabled or disabled via a flip-flop called IEN
The interrupt enable flip-flop IEN can be set and cleared with two instructions (IOF, ION):
  IOF: IEN  0 (the computer cannot be interrupted)
  ION: IEN  1 (the computer can be interrupted)
Video Box Position

## Slide 62: Program Interruptcont.
Another flip-flop (called the interrupt flip-flop R) is used in the computer’s interrupt facility to decide when to go through the interrupt cycle
FGI and FGO are different here compared to the way they acted in an earlier discussion!!
So, the computer is either in an Instruction Cycle or in an Interrupt Cycle
Video Box Position

## Slide 63: Program Interruptcont.
The interrupt cycle is a hardware implementation of a branch and save return address operation (BSA)
The return address available in PC is stored in a specific location where it can be found later when the program returns to the instruction at which it was interrupted
This location may be a processor register, a memory stack, or a specific memory location
Video Box Position

## Slide 64: Program Interruptcont.
For our computer, we choose the memory location at address 0 as a place for storing the return address
Control then inserts address 1 into PC: this means that the first instruction of the interrupt service routine should be stored in memory at address 1, or, the programmer must store a branch instruction that sends the control to an interrupt service routine!!
Video Box Position

## Slide 65: Program Interruptcont.
Video Box Position
IEN
=0
=1
R = Interrupt flip-flop
Store return address
=1
=0
in location 0
M[0]  PC
Branch to location 1
PC  1
IEN  0
R  0
Interrupt cycle
Instruction cycle
Fetch and decode
instructions
Execute
instructions
R  1
=1
=1
=0
=0
FGI
FGO
R
Flowchart for interrupt cycle

## Slide 66: Program Interruptcont.
IEN, R  0: no more interruptions can occur until the interrupt request from the flag has been serviced
The service routine must end with an instruction that re-enables the interrupt (IEN  1) and an instruction to return to the instruction at which the interrupt occurred
The instruction that returns the control to the original program is "indirect BUN 0"
Video Box Position

## Slide 67: Program Interruptcont.
Video Box Position
Example: the computer is interrupted during execution of the instruction at address 255
After interrupt cycle
0
BUN
1120
0
1
PC = 256
255
1
BUN
0
Before interrupt
Main
Program
1120
I/O
Program
0
BUN
1120
0
PC = 1
256
255
1
BUN
0
Memory
Main
Program
1120
I/O
Program
256

## Slide 68: Interrupt Cycle
The fetch and decode phases of the instruction cycle must be :
(Replace T0, T1, T2  R'T0, R'T1, R'T2 (fetch and decode phases occur at the instruction cycle when R = 0)
Interrupt Cycle:
  RT0: AR  0, TR  PC
  RT1: M[AR]  TR, PC  0
  RT2: PC  PC + 1, IEN  0, R  0, SC  0
Video Box Position

## Slide 69: Complete computer description
Video Box Position

## Slide 71: Design of Basic Computer

## Slide 72: Control Logic Gates

## Slide 73: Control of Register and Memory

## Slide 74: Designing of Accumulator

## Slide 75: Designing of Accumulator

## Slide 76: Designing of Accumulator

## Slide 77: Control Unit Implementation
Video Box Position
Hardwired
Microprogrammed
Instruction code
Combinational
Logic Circuits
Memory
Sequence Counter
.
.
Control
signals
Control
signals
Next Address
Generator
(sequencer)
CAR
Control
Memory
CDR
Decoding
Circuit
Memory
.
.
CAR: Control Address Register
CDR: Control Data Register
Instruction code

## Slide 78: Microprogrammed Control Unit
Video Box Position
Control signals
  Group of bits used to select paths in multiplexers, decoders,
  arithmetic logic units
Control variables
  Binary variables specify microoperations
    Certain microoperations initiated while others idle
Control word
  String of 1’s and 0’s represent control variables

## Slide 79: Microprogrammed Control Unit
Control memory
  Memory contains control words
Microinstructions
  Control words stored in control memory
  Specify control signals for execution of microoperations
Microprogram
  Sequence of microinstructions
Video Box Position

## Slide 80: Microprogrammed Control Unit
Read-only memory (ROM)
Content of word in ROM at given address specifies microinstruction
Each computer instruction initiates series of microinstructions (microprogram) in control memory
These microinstructions generate microoperations to
  Fetch instruction from main memory
  Evaluate effective address
  Execute operation specified by instruction
  Return control to fetch phase for next instruction
Video Box Position
Control memory (ROM)
Control word (microinstruction)
Address

## Slide 81: Microprogrammed Control Unit
Control memory
  Contains microprograms (set of microinstructions)
  Microinstruction contains
    Bits initiate microoperations
    Bits determine address of next microinstruction
Control address register (CAR)
  Specifies address of next microinstruction
Video Box Position
Control
word
Next Address
Generator
(sequencer)
CAR
Control
Memory
(ROM)
CDR
External
input

## Slide 82: Microprogrammed Control Organization
Next address generator (microprogram sequencer)
  Determines address sequence for control memory
Microprogram sequencer functions
  Increment CAR by one
  Transfer external address into CAR
  Load initial address into CAR to start control operations
Video Box Position

## Slide 83: Microprogrammed Control Organization
Control data register (CDR)- or pipeline register
  Holds microinstruction read from control memory
  Allows execution of microoperations specified by control word simultaneously with generation of next microinstruction
Control unit can operate without CDR
Video Box Position
Control
word
Next Address
Generator
(sequencer)
CAR
Control
Memory
(ROM)
External
input

## Slide 85: Address Sequencing
Video Box Position
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)
Subroutine
Register
(SBR)
Branch
logic
Status
bits
Microoperations
Control Address Register
(CAR)
Incrementer
MUX
select
select a status
bit
Branch address

## Slide 86: Microprogram Routines
Routine
  Group of microinstructions stored in control memory
Each computer instruction has its own microprogram routine to generate microoperations that execute the instruction
Video Box Position

## Slide 87: Microprogram Routines
Subroutine
  Sequence of microinstructions used by other routines to accomplish particular task
Example
  Subroutine to generate effective address of operand for memory reference instruction
Subroutine register (SBR)
  Stores return address during subroutine call
Video Box Position

## Slide 88: Conditional Branching
Branching from one routine to another depends on status bit conditions
Status bits provide parameter info such as
  Carry-out of adder
  Sign bit of number
  Mode bits of instruction
Info in status bits can be tested and actions initiated based on their conditions: 1 or 0
Unconditional branch
  Fix value of status bit to 1
Video Box Position

## Slide 89: Mapping of Instruction
Each computer instruction has its own microprogram routine stored in a given location of the control memory
Mapping
  Transformation from instruction code bits to address in control memory where routine is located
Video Box Position

## Slide 90: Mapping of Instruction
Example
  Mapping 4-bit operation code to 7-bit address
Video Box Position
OP-codes of Instructions
ADD AND
LDA
0000
0001
0010
Address
0 0000 00
0 0001 00
0 0010 00
Mapping bits
0 xxxx 00
ADD Routine
AND Routine
LDA Routine
Control
memory

## Slide 91: Address Sequencing
Address sequencing capabilities required in control unit
  Incrementing CAR
  Unconditional or conditional branch, depending on status bit conditions
  Mapping from bits of instruction to address for control memory
  Facility for subroutine call and return
Video Box Position

## Slide 92: Address Sequencing
Video Box Position
Instruction code
Mapping
logic
Multiplexers
Control memory (ROM)
Subroutine
Register
(SBR)
Branch
logic
Status
bits
Microoperations
Control Address Register
(CAR)
Incrementer
MUX
select
select a status
bit
Branch address

## Slide 93: Microprogram Example
Video Box Position
Computer
Configuration
MUX
AR
10
0
PC
10
0
Address
Memory
2048 x 16
MUX
DR
15
0
Arithmetic
logic and
shift unit
AC
15
0
SBR
6
0
CAR
6
0
Control memory
128 x 20
Control unit

## Slide 94: Microprogram Example
Video Box Position
Microinstruction Format
EA is the effective address
Symbol OP-code Description
  ADD 0000 AC AC + M[EA]
  BRANCH 0001 if (AC < 0) then (PC  EA)
  STORE 0010 M[EA]  AC
  EXCHANGE 0011 AC  M[EA], M[EA]  AC
Computer instruction format
I
Opcode
15
14
11
10
Address
0
Four computer instructions
F1
F2
F3
CD
BR
AD
3
3
3
2
2
7
F1, F2, F3: Microoperation fields
CD: Condition for branching
BR: Branch field
AD: Address field

## Slide 95: Microinstruction Fields
Video Box Position
F1 Microoperation Symbol
000 None NOP
001 AC  AC + DR ADD
010 AC  0 CLRAC
011 AC  AC + 1 INCAC
100 AC  DR DRTAC
101 AR  DR(0-10) DRTAR
110 AR  PC PCTAR
111 M[AR]  DR WRITE
F2 Microoperation Symbol
000 None NOP
001 AC  AC - DR SUB
010 AC  AC  DR OR
011 AC  AC  DR AND
100 DR  M[AR] READ
101 DR  AC ACTDR
110 DR  DR + 1 INCDR
111 DR(0-10)  PC PCTDR
F3 Microoperation Symbol
000 None NOP
001 AC  AC  DR XOR
010 AC  AC’ COM
011 AC  shl AC SHL
100 AC  shr AC SHR
101 PC  PC + 1 INCPC
110 PC  AR ARTPC
111 Reserved

## Slide 96: Microinstruction Fields
Video Box Position
CD Condition Symbol Comments
00 Always = 1 U Unconditional branch
01 DR(15) I Indirect address bit
10 AC(15) S Sign bit of AC
11 AC = 0 Z Zero value in AC
  BR Symbol Function
  00 JMP CAR  AD if condition = 1
  CAR  CAR + 1 if condition = 0
  01 CALL CAR  AD, SBR  CAR + 1 if condition = 1
  CAR  CAR + 1 if condition = 0
  10 RET CAR  SBR (Return from subroutine)
  11 MAP CAR(2-5)  DR(11-14), CAR(0,1,6)  0

## Slide 97: Symbolic Microinstruction
Video Box Position
Sample Format Label: Micro-ops CD BR AD
Label may be empty or may specify symbolic address
terminated with colon
Micro-ops consists of 1, 2, or 3 symbols separated by commas
CD one of {U, I, S, Z}
U: Unconditional Branch
I: Indirect address bit
S: Sign of AC
Z: Zero value in AC
BR one of {JMP, CALL, RET, MAP}
AD one of {Symbolic address, NEXT, empty}

## Slide 98: Fetch Routine
Video Box Position
Fetch routine
  - Read instruction from memory
  - Decode instruction and update PC
AR  PC
DR  M[AR], PC  PC + 1
AR  DR(0-10), CAR(2-5)  DR(11-14), CAR(0,1,6)  0
Symbolic microprogram for fetch routine:
ORG 64
PCTAR U JMP NEXT
READ, INCPC U JMP NEXT
DRTAR U MAP
FETCH:
Binary microporgram for fetch routine:
1000000 110 000 000 00 00 1000001
1000001 000 100 101 00 00 1000010
1000010 101 000 000 00 11 0000000
Binary
address F1 F2 F3 CD BR AD
Microinstructions for fetch routine:

## Slide 99: Symbolic Microprogram
Video Box Position
Control memory: 128 20-bit words
First 64 words: Routines for 16 machine instructions
Last 64 words: Used for other purpose (e.g., fetch routine and other subroutines)
Mapping: OP-code XXXX into 0XXXX00, first address for 16 routines are
0(0 0000 00), 4(0 0001 00), 8, 12, 16, 20, ..., 60
ORG 0
NOP
READ
ADD
ORG 4
NOP
NOP
NOP
ARTPC
ORG 8
NOP
ACTDR
WRITE
ORG 12
NOP
READ
ACTDR, DRTAC
WRITE
ORG 64
PCTAR
READ, INCPC
DRTAR
READ
DRTAR
I
U
U
S
U
I
U
I
U
U
I
U
U
U
U
U
U
U
U
CALL
JMP
JMP
JMP
JMP
CALL
JMP
CALL
JMP
JMP
CALL
JMP
JMP
JMP
JMP
JMP
MAP
JMP
RET
INDRCT
NEXT
FETCH
OVER
FETCH
INDRCT
FETCH
INDRCT
NEXT
FETCH
INDRCT
NEXT
NEXT
FETCH
NEXT
NEXT
NEXT
ADD:
BRANCH:
OVER:
STORE:
EXCHANGE:
FETCH:
INDRCT:
Label Microops CD BR AD
Partial Symbolic Microprogram

## Slide 100: Binary Microprogram
Video Box Position
  Address Binary Microinstruction
  Micro Routine Decimal Binary F1 F2 F3 CD BR AD
ADD 0 0000000 000 000 000 01 01 1000011
  1 0000001 000 100 000 00 00 0000010
  2 0000010 001 000 000 00 00 1000000
  3 0000011 000 000 000 00 00 1000000
BRANCH 4 0000100 000 000 000 10 00 0000110
  5 0000101 000 000 000 00 00 1000000
  6 0000110 000 000 000 01 01 1000011
  7 0000111 000 000 110 00 00 1000000
STORE 8 0001000 000 000 000 01 01 1000011
  9 0001001 000 101 000 00 00 0001010
  10 0001010 111 000 000 00 00 1000000
  11 0001011 000 000 000 00 00 1000000
EXCHANGE 12 0001100 000 000 000 01 01 1000011
  13 0001101 001 000 000 00 00 0001110
  14 0001110 100 101 000 00 00 0001111
  15 0001111 111 000 000 00 00 1000000
FETCH 64 1000000 110 000 000 00 00 1000001
  65 1000001 000 100 101 00 00 1000010
  66 1000010 101 000 000 00 11 0000000
INDRCT 67 1000011 000 100 000 00 00 1000100
  68 1000100 101 000 000 00 10 0000000

## Slide 101: Design of Control Unit
Video Box Position
microoperation fields
3 x 8 decoder
7
6
5
4
3
2
1
0
F1
3 x 8 decoder
7
6
5
4
3
2
1
0
F2
3 x 8 decoder
7
6
5
4
3
2
1
0
F3
Arithmetic
logic and
shift unit
AND
ADD
DRTAC
AC
Load
From
PC
From
DR(0-10)
Select
0
1
Multiplexers
AR
Load
Clock
AC
DR
DRTAR
PCTAR

## Slide 102: Microprogram Sequencer
Video Box Position
3
2
1
0
S1
MUX1
External
(MAP)
SBR
Load
Incrementer
CAR
Input
logic
I0
T
MUX2
Select
1
I
S
Z
Test
Clock
Control memory
Microops
CD
BR
AD
L
I1
S0
. . .
. . .

## Slide 103: Input Logic for Microprogram Sequencer
Video Box Position
Input
logic
I0
I1
T
MUX2
Select
1
I
S
Z
Test
CD Field of CS
From
CPU
BR field
of CS
L(load SBR with PC) for subroutine Call
S0
S1
for next address
selection
I1I0T Meaning Source of Address S1S0 L
000 In-Line CAR+1 00 0
001 JMP CS(AD) 01 0
010 In-Line CAR+1 00 0
011 CALL CS(AD) and SBR <- CAR+1 01 1
10x RET SBR 10 0
11x MAP DR(11-14) 11 0
L
S1 = I1
S0 = I0I1 + I1’T
L = I1’I0T
Input Logic