## Slide 1: CENTRAL PROCESSING UNIT
  Introduction
  General Register Organization
  Stack Organization
  Instruction Formats
  Addressing Modes
  Data Transfer and Manipulation
  Program Control
  Reduced Instruction Set Computer (RISC)
Video Box Position

## Slide 2: MAJOR COMPONENTS OF CPU
Video Box Position
Register
File
ALU
Control Unit
Storage Components:
Registers
Flip-flops
Execution (Processing) Components:
Arithmetic Logic Unit (ALU):
Arithmetic calculations, Logical computations, Shifts/Rotates
Transfer Components:
Bus
Control Components:
Control Unit

## Slide 3: GENERAL REGISTER ORGANIZATION
Video Box Position
MUX
SELA
{
MUX
}
SELB
ALU
OPR
R1
R2
R3
R4
R5
R6
R7
Input
3 x 8
decoder
SELD
Load
(7 lines)
Output
A bus
B bus
Clock

## Slide 4: OPERATION OF CONTROL UNIT
Video Box Position
The control unit directs the information flow through ALU by:
- Selecting various Components in the system
- Selecting the Function of ALU
Example: R1 <- R2 + R3
[1] MUX A selector (SELA): BUS A  R2
[2] MUX B selector (SELB): BUS B  R3
[3] ALU operation selector (OPR): ALU to ADD
[4] Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
  Binary
  Code SELA SELB SELD
  000 Input Input None
  001 R1 R1 R1
  010 R2 R2 R2
  011 R3 R3 R3
  100 R4 R4 R4
  101 R5 R5 R5
  110 R6 R6 R6
  111 R7 R7 R7
SELA
SELB
SELD
OPR
3
3
3
5

## Slide 5: ALU CONTROL
Video Box Position
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
  R1  R2 - R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100
  R1  R2 - R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100

## Slide 6: REGISTER STACK ORGANIZATION
Video Box Position
cpe 252: Computer Organization
6
Register Stack
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP - 1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Very useful feature for nested subroutines, nested loops control
- Also efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack

## Slide 7: MEMORY STACK ORGANIZATION
Video Box Position
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
- Most computers do not provide hardware to check
stack overflow (full stack) or underflow(empty stack)
Memory with Program, Data,
and Stack Segments
DR
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack

## Slide 8: REVERSE POLISH NOTATION
Video Box Position
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 9: INSTRUCTION FORMAT
Video Box Position
OP-code field - specifies the operation to be performed
Address field - designates memory address(s) or a processor register(s)
Mode field - specifies the way the operand or the
effective address is determined
The number of address fields in the instruction format
depends on the internal organization of CPU
- The three most common CPU organizations:
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 10: THREE, and TWO-ADDRESS INSTRUCTIONS
Video Box Position
Three-Address Instructions:
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions:
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[B] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 11: ONE, and ZERO-ADDRESS INSTRUCTIONS
Video Box Position
cpe 252: Computer Organization
11
One-Address Instructions:
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions:
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 12: ADDRESSING MODES
Video Box Position
Addressing Modes:
* Specifies a rule for interpreting or modifying the
address field of the instruction (before the operand
is actually referenced)
* Variety of addressing modes
- to give programming flexibility to the user
- to use the bits in the address field of the
instruction efficiently

## Slide 13: TYPES OF ADDRESSING MODES
Video Box Position
Implied Mode
Address of the operands are specified implicitly
in the definition of the instruction
- No need to specify address in the instruction
- EA = AC, or EA = Stack[SP], EA: Effective Address.
Immediate Mode
Instead of specifying the address of the operand,
operand itself is specified
- No need to specify address in the instruction
- However, operand itself needs to be specified
- Sometimes, require more bits than the address
- Fast to acquire an operand
Register Mode
Address specified in the instruction is the register address
- Designated operand need to be in a register
- Shorter address than the memory address
- Saving address field in the instruction
- Faster to acquire an operand than the memory addressing
- EA = IR(R) (IR(R): Register field of IR)

## Slide 14: TYPES OF ADDRESSING MODES
Video Box Position
Register Indirect Mode
Instruction specifies a register which contains
the memory address of the operand
- Saving instruction bits since register address
is shorter than the memory address
- Slower to acquire an operand than both the
register addressing or memory addressing
- EA = [IR(R)] ([x]: Content of x)
Auto-increment or Auto-decrement features:
Same as the Register Indirect, but:
- When the address in the register is used to access memory, the value in the register is incremented or decremented by 1 (after or before the execution of the instruction)

## Slide 15: TYPES OF ADDRESSING MODES
Video Box Position
Direct Address Mode
Instruction specifies the memory address which
can be used directly to the physical memory
- Faster than the other memory addressing modes
- Too many bits are needed to specify the address
for a large physical memory space
- EA = IR(address), (IR(address): address field of IR)
Indirect Addressing Mode
The address field of an instruction specifies the address of a memory location that contains the address of the operand
- When the abbreviated address is used, large physical memory can be addressed with a relatively small number of bits
- Slow to acquire an operand because of an additional memory access
- EA = M[IR(address)]

## Slide 16: TYPES OF ADDRESSING MODES
Video Box Position
Relative Addressing Modes
The Address fields of an instruction specifies the part of the address (abbreviated address) which can be used along with a designated register to calculate the address of the operand
PC Relative Addressing Mode(R = PC)
- EA = PC + IR(address)
- Address field of the instruction is short
- Large physical memory can be accessed with a small number of address bits
Indexed Addressing Mode
XR: Index Register:
- EA = XR + IR(address)
Base Register Addressing Mode
BAR: Base Address Register:
- EA = BAR + IR(address)

## Slide 17: ADDRESSING MODES - EXAMPLES
Video Box Position
Addressing
Mode
Effective
Address
Content
of AC
Load to AC Mode
Address = 500
Next instruction
200
201
202
399
400
450
700
500
800
600
900
702
325
800
300
Memory
Address
PC = 200
R1 = 400
XR = 100
AC
  Direct address 500 /* AC  (500) */ 800
  Immediate operand - /* AC  500 */ 500
  Indirect address 800 /* AC  ((500)) */ 300
  Relative address 702 /* AC  (PC+500) */ 325
  Indexed address 600 /* AC  (XR+500) */ 900
  Register - /* AC  R1 */ 400
  Register indirect 400 /* AC  (R1) */ 700
  Autoincrement 400 /* AC  (R1)+ */ 700
  Autodecrement 399 /* AC  -(R) */ 450

## Slide 18: DATA TRANSFER INSTRUCTIONS
Video Box Position
Load LD
Store ST
Move MOV
Exchange XCH
Input IN
Output OUT
Push PUSH
Pop POP
Name Mnemonic
Typical Data Transfer Instructions
Direct address LD ADR AC M[ADR]
Indirect address LD @ADR AC  M[M[ADR]]
Relative address LD $ADR AC  M[PC + ADR]
Immediate operand LD #NBR AC  NBR
Index addressing LD ADR(X) AC  M[ADR + XR]
Register LD R1 AC  R1
Register indirect LD (R1) AC  M[R1]
Autoincrement LD (R1)+ AC  M[R1], R1  R1 + 1
Autodecrement LD -(R1) R1  R1 - 1, AC  M[R1]
Mode
Assembly
Convention
Register Transfer
Data Transfer Instructions with Different Addressing Modes

## Slide 19: DATA MANIPULATION INSTRUCTIONS
Video Box Position
Three Basic Types:
Arithmetic instructions
Logical and bit manipulation instructions
Shift instructions
Arithmetic Instructions
Name Mnemonic
Clear CLR
Complement COM
AND AND
OR OR
Exclusive-OR XOR
Clear carry CLRC
Set carry SETC
Complement carry COMC
Enable interrupt EI
Disable interrupt DI
Name Mnemonic
Logical shift right SHR
Logical shift left SHL
Arithmetic shift right SHRA
Arithmetic shift left SHLA
Rotate right ROR
Rotate left ROL
Rotate right thru carry RORC
Rotate left thru carry ROLC
Name Mnemonic
Logical and Bit Manipulation Instructions
Shift Instructions
Increment INC
Decrement DEC
Add ADD
Subtract SUB
Multiply MUL
Divide DIV
Add with Carry ADDC
Subtract with Borrow SUBB
Negate(2’s Complement) NEG

## Slide 20: PROGRAM CONTROL INSTRUCTIONS
Video Box Position
PC
+1
In-Line Sequencing
(Next instruction is fetched from the
next adjacent location in the memory)
Address from other source; Current Instruction, Stack, etc
Branch, Conditional Branch, Subroutine, etc
Program Control Instructions
Name Mnemonic
Branch BR
Jump JMP
Skip SKP
Call CALL
Return RTN
Compare(by - ) CMP
Test (by AND) TST
* CMP and TST instructions do not retain their
results of operations(- and AND, respectively).
They only set or clear certain Flags.
Status Flag Circuit
c7
c8
A B
8 8
8-bit ALU
V Z S C
F7
F7 - F0
8
F
Check for
zero output

## Slide 21: CONDITIONAL BRANCH INSTRUCTIONS
Video Box Position
BZ Branch if zero Z = 1
BNZ Branch if not zero Z = 0
BC Branch if carry C = 1
BNC Branch if no carry C = 0
BP Branch if plus S = 0
BM Branch if minus S = 1
BV Branch if overflow V = 1
BNV Branch if no overflow V = 0
BHI Branch if higher A > B
BHE Branch if higher or equal A  B
BLO Branch if lower A < B
BLOE Branch if lower or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
BGT Branch if greater than A > B
BGE Branch if greater or equal A  B
BLT Branch if less than A < B
BLE Branch if less or equal A  B
BE Branch if equal A = B
BNE Branch if not equal A  B
Unsigned compare conditions (A - B)
Signed compare conditions (A - B)
Mnemonic Branch condition Tested condition

## Slide 22: SUBROUTINE CALL AND RETURN
Video Box Position
Call subroutine
Jump to subroutine
Branch to subroutine
Branch and save return address
Fixed Location in the subroutine(Memory)
Fixed Location in memory
In a processor Register
In a memory stack
- most efficient way
SUBROUTINE CALL
Two Most Important Operations are Implied;
* Branch to the beginning of the Subroutine
- Same as the Branch or Conditional Branch
* Save the Return Address to get the address
of the location in the Calling Program upon
exit from the Subroutine
- Locations for storing Return Address:
CALL
SP  SP - 1
M[SP]  PC
PC  EA
RTN
PC  M[SP]
SP  SP + 1

## Slide 23: PROGRAM INTERRUPT
Video Box Position
Types of Interrupts:
External interrupts
External Interrupts initiated from the outside of CPU and Memory
- I/O Device -> Data transfer request or Data transfer complete
- Timing Device -> Timeout
- Power Failure
Internal interrupts (traps)
Internal Interrupts are caused by the currently running program
- Register, Stack Overflow
- Divide by zero
- OP-code Violation
- Protection Violation
Software Interrupts
Both External and Internal Interrupts are initiated by the computer Hardware.
Software Interrupts are initiated by texecuting an instruction.
- Supervisor Call -> Switching from a user mode to the supervisor mode
-> Allows to execute a certain class of operations
which are not allowed in the user mode

## Slide 24: INTERRUPT PROCEDURE
Video Box Position
  - The interrupt is usually initiated by an internal or
  an external signal rather than from the execution of
  an instruction (except for the software interrupt)
  - The address of the interrupt service program is
  determined by the hardware rather than from the
  address field of an instruction
  - An interrupt procedure usually stores all the
  information necessary to define the state of CPU
  rather than storing only the PC.
  The state of the CPU is determined from;
  Content of the PC
  Content of all processor registers
  Content of status bits
  Many ways of saving the CPU state depending on the CPU architectures
Interrupt Procedure and Subroutine Call

## Slide 25: Parallel Processing

## Slide 26: Processor with multiple functional units

## Slide 27: Classification of computer architecture by M J Flynn

## Slide 28: Pipelining

## Slide 29: Example of Pipelining

## Slide 30: Pipeline

## Slide 31: Four Segment Pipeling

## Slide 32: Arithmetic Pipeline

## Slide 33: Arithmetic Pipeline

## Slide 34: Arithmetic Pipeline

## Slide 35: Instruction Pipeline

## Slide 36: Instruction Pipeline

## Slide 37: Instruction Pipeline

## Slide 38: Disadvantages
Resource Conflicts
Data dependency Conflicts
Branch Difficulties

## Slide 39: Addition And Subtraction of Signed Magnitude Numbers

## Slide 40: Hardware Implementation

## Slide 41: Flow Chart For Addition and Subtraction

## Slide 42: Signed 2’s Complement Addition and Subtraction

## Slide 43: Decimal arithmetic Unit

## Slide 44: Decimal arithmetic Unit

## Slide 45: Block Diagram of BCD Adder

## Slide 46: BCD Subtraction

## Slide 47: Decimal arithmetic Unit

## Slide 48: Multiplication of Signed-Magnitude data

## Slide 49: Multiplication of Signed-Magnitude data

## Slide 50: Example

## Slide 51: Multiplication of Signed-Magnitude data

## Slide 52: Booth Multiplication Algorithm

## Slide 53: Booth Multiplication Algorithm

## Slide 54: Booth Multiplication Algorithm

## Slide 55: Booth Multiplication Algorithm